## Slide 1
Transmission Control Protocol (TCP)

## Slide 2
Transmission Control Protocol (TCP)
•
If the Internet Protocol (IP) is thought of as the protocol for
getting information from a sending machine to a receiving
machine, then Transmission Control Protocol (TCP) can be
thought of as directing the transmitted packet to the correct
program on the receiving machine.
•
As you might imagine, it is important to be able to identify
both
where
the receiver is and
what
the packet is for, so TCP
and IP are almost an inseparable pair: TCP/IP.

## Slide 3
Transmission Control Protocol (TCP)
•
Each program/utility/service on a machine is assigned a
port
number
. Coupled with anIP address, we can now uniquely
identify a specific program on a specific machine.
•
The other thing that TCP is crucial for is
guaranteeing delivery
of packets, which IP alone does not do.
•
TCP does this by including information about how many
packets the receiver should expect to get, and in what order,
and transmitting that information alongside the data.

## Slide 4
Transmission Control Protocol (TCP)
•
Some ports are so commonly usedthat they have been
standardized across all computers.
•
FTP (file transfer) uses port
21
.
•
SMTP (e-mail) uses port
25
.
•
DNS uses port
53
.
•
HTTP (web browsing) uses port
80
.
•
HTTPS (secure web browsing) uses post
443
.

## Slide 5
Transmission Control Protocol (TCP)
•
Steps of the TCP/IP process
1.
When a program goes to send data, TCP breaks it into smaller
chunks and communicates those packets to the computer’s
network software, adding a TCP layer onto the packet.
2.
IP routes the individual packets from senderto receiver; this info is
part of the IP layer surrounding the packet.
3.
When the destination computer gets the packet, TCP looks at the
header to see which program it belongs to; and since the routes
packets take may differ, TCP also must present those packets to the
destination program in the proper order.

## Slide 6
Transmission Control Protocol (TCP)
e-mail
SENDER
RECEIVER

## Slide 7
Transmission Control Protocol (TCP)
A
B
C
D
SENDER
RECEIVER

## Slide 8
Transmission Control Protocol (TCP)
A
B
C
D
SENDER
RECEIVER

## Slide 9
Transmission Control Protocol (TCP)
<DATA>
A
B
C
D
SENDER
RECEIVER

## Slide 10
Transmission Control Protocol (TCP)
25 / 1 of 4
<DATA>
A
B
C
D
SENDER
RECEIVER